## Slide 1: Cross-comparison tools for LIS, LMA, and VLF/LF Ground-based Network Data
Ken Cummins1,
with help from:
Richard J. Blakeslee2 , Lawrence D. Carey3,
Jeff C. Bailey3, Monte Bateman4, Steven J. Goodman5
1 University of Arizona, Tucson, Arizona
2 NASA Marshall Space Flight Center, Huntsville, Alabama
3 University of Alabama in Huntsville, Huntsville, Alabama
4 USRA, Huntsville, Alabama
5 NOAA NESDIS, Greenbelt, Maryland
GLM Stakeholders Workshop 2014

## Slide 2: Context
Requirement
  Ground-base lightning observations are needed to help create GLM proxy and ground-validation datasets over large continental and oceanic regions
Some Approaches
  “bulk statistical analysis of datasets at the cell flash-rate level
  Detailed stroke/pulse inter-comparisons to understand what is seen uniquely and in-common by various data sources (this work)
Issue
  LLS performance for CG strokes and cloud pulses must be characterized before it can be intelligently applied
    Location accuracy
    Detection efficiency
    Type classification (CLD/CG)
  Sub-context: CHUVA LLS inter-comparisons

## Slide 3: What sorts of tools?
Statistical LLS Inter-comparison Tools
  Stroke/pulse level
  Flash level
  Available for community use (supported by NASA)
    Fully documented
Exploration Tools
  Described in CHUVA Workshop abstract (Cummins et al.)
  Similar to DLR tools
  Detailed flash-level visual exploration
    LIS groups
    LMA sources
    VLF/LF strokes and cloud pulses

## Slide 4: LLS Inter- comparison Tool
Coded in Matlab
Stand-alone executables can run on Unix, Linux, and Windows
Can specify datasets and related parameters in a “cfg” file using a text editor…

## Slide 5: Tool “Outputs”
Analysis “Sheets”
  Sheet 1:
    Requires date, time, lat, lon, and (optionally) type (CG/CLD pulse)
  Sheet 2:
    Requires peak current estimates
  Sheet 3:
    Requires quality-related parameters
      location error estimate
      # sensors reporting the stroke/pulse
Spatial Detection Efficiency
Flash Analysis

## Slide 6: Spatial Detection Efficiency
Observe spatial variation in DE
  Combined for cloud pulses and CG strokes
Helpful for selecting LLS comparison regions
Automatic global country/coastline
Example: CHUVA TLS200cg (ref) and GLD360 (test)

## Slide 7: Flash Analysis Overview
  Definition of flash DE
  This is complicated by the fact that LLS’s frequently disagree about the discharge type (cloud vs. CG)
TestCLD
TestCG
ReferenceCLD
ReferenceCG
TestCLDFmatchRefCG
TestCGFmatchRefCG
TestCLDFmatchRefCLD
TestCGFmatchRefCLD
DE_TestCGF = 100.*(TestCGFmatchRefCG + TestCLDFmatchRefCG) /(RefCGF);
DE_TestAll = 100.*allMatchTest/(RefCGF+RefCLDF);
Examples:
Details

## Slide 8: Additional Flash Analysis: where (in time) are the LLS cloud pulses detected?
The Flash Analysis includes a temporal analysis for each network
  Are they part of a cloud flash?
  Are they part of a CG flash?
  What part of a CG flash?
“pre”
“during”
“cld”
Cloud flash
CG flash
Back

## Slide 9: Flash – CHUVA LINET vs. GLD360

## Slide 10: How to get the stuff…
http://Atmo.Arizona.edu/~lightning/NASA/Compare/

## Slide 11: Example Use: LIS-referenced DE
Simple question: When LIS saw something, did others see it?
METHOD:
  Selected a “common” (small) region and time period
    Region determined by LINET
    Time period limit defined by TLS200
      January 1 through March 27, 2012
        Note: LINET is compromised during these times
    Total Groups/Flashes were ~2900/300 in 13 overpasses
  Use tools to compute group-referenced and Flash-referenced DE
    Produce flashes from LIS Groups and LLS “events”
      Multiple IPI/Distance Criteria for flash grouping: (200 ms/20 km; 500 ms/30 km; 500 ms /50 km for some long-range networks)

## Slide 12: Selection of the Analysis Domain
Smaller domain would not have enough LIS flashes ( < 300)
The domain is quite large for LINET
  confirmed that the LINET pulse/stroke DE, relative to TLS-LF-all, was not compromised over this domain

## Slide 13: Sheet 1 – LIS Groups vs. GLD360

## Slide 14: Flash Summary Statistics
Flash Grouping (IPI/Dist) | LLS Network | Relative Group DE | Relative Flash DE | Mean Groups/fl | Mean Mult. (G/C) | Nominal Sensor Baseline in test region
200/20 | LINET | 32.0 | 61 | 8.4 | 3.3/3.2 | 22-45 km
200/20 | TLS-LF “all” | 23 | 56 | 8.4 | 2.9/2.5 | 55-125 km
200/20 | BrasilDat | 15 | 45 | 8.4 | 1.8/3.3 | ~100 km
200/20 | GLD360 | 5 | 17 | 8.4 | 2.4/0.0 | >big
200/20 | TLS-LF CG | 6 | 13 | 8.4 | 3.3/0.0 | 55-125 km
200/20 | StarNet | 2 | 8 | 8.4 | 1.6/0.0 | >big
200/20 | WWLLN | 1 | 2 | 8.4 | 1.7/0.0 | >big
(estimated uncertainty of about +/-2%) |  |  |  |  |  | 
500/30 | LINET | 32 | 67 | 9.2 | 3.5/3.4 | 22-45 km
500/30 | TLS-LF “all” | 23 | 67 | 9.2 | 3.0/2.8 | 55-125 km
500/30 | BrasilDat | 15 | 53 | 9.2 | 1.8/3.6 | ~100 km
500/30 | GLD360 | 5 | 24 | 9.2 | 2.8/0.0 | >big
500/30 | TLS-LF CG | 6 | 19 | 9.2 | 3.5/0.0 | 55-125 km
500/50 | StarNet | 2 | 14 | 10.3 | 2.0/0.0 | >big
500/50 | WWLLN | 1 | 5 | 10.4 | 2.0/0.0 | >big

## Slide 15: Comments from data contributors
WWLLN
  The small domain and small number of flashes result in uncertainty in the WWLLN findings. Analysis over a larger domain should be done
LINET
  During much of this time, only 5 of the 7 sensors were operational.
  Leap-second issue with LIS data?
BrasilDat
  Typically, only 1-2 of the 7 “special” sites were operational, and the network was just being calibrated. The network is now working much better than it was during the CHUVA campaign. ( the ~100 km baseline in the previous slide reflected the “functional” baseline during this study)

## Slide 16: Summary / Comments
LLS Relative Performance vs. LIS Total Lightning
  Wide variation in TL flash DE (few percent => ~70%)
  Short-baseline VLF/LF networks CAN detect a majority of TL flashes (but do not represent the spatial extent of big flashes)
    Note: Hartmut indicates that for days with all LINET sensors working, they would detect almost all LIS flashes that were within the network, as well as some flashes not reported by LIS
  Some long-range LF networks MIGHT be sufficiently good to allow statistical up-scaling of the data for mid-oceanic LIS proxy and validation activities

## Slide 17: End of talk…
Thanks!

## Slide 18: Sheet 1 – two networks in Japan
Next

## Slide 19: Sheet 1 – GLD360 vs. NALDN
Back

## Slide 20: Sheet 2 – two networks in Japan
Next

## Slide 21: Sheet 2 – GLD360 vs. NALDN
Back

## Slide 22: Sheet 3 – two networks in Japan
Next

## Slide 23: Sheet 3 – GLD360 vs. NALDN
Back

## Slide 24: Flash Analysis Overview
Flash Grouping (within an individual LLS dataset)
  New flash is initiated if there are no “active” flashes within the max inter-pulse interval (IPI) and within the max separation distance (typically 200 mS and10 km for “accurate” LLS’s)
  If there is a match with more than one active flash, then the new pulse is added to the flash with the spatially-closest pulse
  A flash is “closed” if the time between the most-recent pulse and the first pulse in the flash is greater then the max flash duration (typically 1 second)
Next

## Slide 25: Flash Analysis Overview
Flash / Pulse “Typing”
  Pulses within a CG flash are categorized as one of three types:
    “pre” cloud: likely preliminary breakdown or leader pulse
    “during” cloud: k-changes etc.
    “CG” stroke: we think we knew what this is…
  Any flash containing a CG stroke is a CG flash
A flash is detected in-common by two LLS’s if:
  Any pulse in the flash is matched using the tight requirements employed by the Inter-comparison Tool
  Any “unmatched” pulses in the flash meet the max IPI/Distance requirements when compared to any pulse from the other LLS
Next

## Slide 26: Time-height Analysis of LIS, LMA, and LINET
Back