## Slide 1: Deriving Atmospheric Winds from GOES-R ABI Measurements
Jaime Daniels (Presented by Jeff Key)
Center for Satellite Applications and Research
National Environmental Satellite Data and Information Surface
National Oceanic and Atmospheric Administration
1

## Slide 2: Outline
Background
  Importance of satellite wind observations
  GOES-R capabilities expected impacts on derived winds
Brief overview of the GOES-R nested tracking winds algorithm
Product examples and assessing product quality
User Readiness Activities for GOES-R Winds
2

## Slide 3: Background
  Importance of satellite wind observations
  GOES-R capabilities expected impacts on derived winds
3

## Slide 4: Importance of Satellite Wind Observations
Global Radiosonde Network
Aircraft Winds
4
Satellite Derived Winds are a Key Component of the Global Observing System (GOS)
Provide vital tropospheric wind information over expansive regions of the earth that are devoid of in-situ wind observations that include oceans, polar regions, and Southern Hemisphere land masses.
Provide key wind observations to operational NWP data assimilation systems where their use has been demonstrated to improved numerical weather prediction forecasts including tropical cyclones
Provide key wind observations to NWS field forecasters at NWS WFOs and National Centers
  Situational awareness of wind field
  Verification of model output

## Slide 5: Coordinated Study of AMV Impact Highlights from IWWG Study...
Forecast Sensitivity to Observations (FSO)
Adjoint-based FSO method gives estimate of the contribution of each observation towards reducing the 24-hour forecast error
Satellite winds reduce 24 hour forecast error on the order of 7-11% (NRL was exception)
Places satellite winds among the top global observing system observations that contribute in a positive way to NWP global forecast impact
ECMWF
Met Office
Chart: 
| SYNOP | SHIP-BUOY | TEMP-T | TEMP wind | TEMP-q | Aircraft T | Aircraft wind | AMV | SCAT SFC WIND | AMSU-A | MHS | SSMIS | SSMIS-TPW | SSMIS SFC WIND | WINDSAT-TPW | WINDSAT SFC WIND | IASI | AQUA | GPS | TC Synth
 | -7.2124 | -3.8856 | -2.7819 | -6.3926 | -2.6288 | -6.4419 | -4.9928 | -23.7917 | -1.528 | -7.9447 | -2.6208 | -10.0295 | -4.5469 | -1.1798 | -0.67055 | -0.43786 | -5.8407 | -4.5356 | -2.481 | -0.056546
NRL
5
Notes: IWWG study done in 2012

## Slide 6: How will the GOES-R ABI improve our ability to retrieve better wind products?
6
Higher Spectral Resolution
  Improved cloud detection and cloud retrievals
Higher Spatial Resolution
  Able to retrieve motion at smaller scales
Higher Temporal Resolution
  Improved feature tracking
Improved Radiometrics
  Improved tracking
  Improved AMV height assignments
Improved Navigation and Registration
  Improved tracking
All of these things contribute to one being able to observe and retrieve phenomenon not previously observed before
GOES-14 provided very unique information and offers a glimpse into the possibilities that will be provided by the ABI on GOES-R.

## Slide 7: ABI Bands Used to Derive Winds
7
ABI Band | Center Frequency (um) | Target Scene Size (Lines x Elements) | Horiz. Res (km) | Image Time Interval (mins) | Refresh Rate (mins)
2 | 0.64 | 15x15 | 7.5 | Full Disk: 5 or 15 CONUS: 5 Meso: 5 | Full Disk: 60 CONUS: 15 Meso: 5
7 | 3.90 | 15x15 | 30 | Full Disk: 5 or 15 CONUS: 5 Meso: 5 | Full Disk: 60 CONUS: 15 Meso: 5
8 (Cloudy targets) ------------------------ 8 (Clear-air targets) | 6.15 | 15x15 | 30 | Full Disk: 5 or 15 CONUS: 5 Meso: 5 ----------------------- Full Disk, CONUS, Meso: 30 | Full Disk: 60 CONUS: 15 Meso: 5
9 | 7.0 | 15x15 | 30 | Full Disk, CONUS, Meso: 30 | Full Disk: 60 CONUS: 15 Meso: 5
10 | 7.4 | 15x15 | 30 | Full Disk, CONUS, Meso: 30 | Full Disk: 60 CONUS: 15 Meso: 5
14 | 11.2 | 19x19 | 38 | Full Disk: 5 or 15 CONUS: 5 Meso: 5 | Full Disk: 60 CONUS: 15 Meso: 5

## Slide 8: How will the GOES-R ABI improve our ability to retrieve better wind products?
Improved Navigation
and Registration
Will lead to a more
accurate wind product
GOES-15 provides a hint
of ABI’s INR quality…
8

## Slide 9: How will the GOES-R ABI improve our ability to retrieve better wind products?
100
200
300
400
500
600
700
800
900
1000
0
20
40
60
m/s
Pressure (hPa)
u component (truth)
16 m/s error
-20
Improved Radiometric
Performance together
with Improved Spectral
and Spatial Resolution
Will lead to improved wind
height assignments and a
more accurate wind
product
9
Poor heights assigned to winds can produce large wind errors, especially in regions of large vertical wind shear
AMV height assignment
Notes: Errors in heights assigned to winds are more problematic if large vertical wind shear exists
1 m/s = ~ 2.2 miles/hour
700mb: ~ 3km
400mb: ~ 7km
100mb: ~ 15km

## Slide 10: Brief overview of the GOES-R nested tracking winds algorithm
10

## Slide 11
Designed to minimize observed slow speed bias of satellite winds; a long standing concern of the NWP community
Computes local motions (white arrows) within a larger target scene.
Clustering algorithm used to analyze local motion displacements. The average of the local motions from largest cluster is the final motion solution (green arrow)
Cloud heights at pixels belonging to the largest cluster are used to assign a representative height to the derived motion wind
10
5
0
-5
m/s
Date
Speed Bias
Mean Vector Difference
Red arrow denotes motion of the entire NxN target scene
SPD: 22.3 m/s
Green arrow denotes average of the largest cluster
SPD: 27.6 m/s
After clustering
Before clustering
GOES-12 Satwinds vs. Rawinsonde (100-400 hPa)
N
N
GOES-R Nested Tracking
Winds Algorithm
11

## Slide 12: Product Examples and Assessing Product Quality
12

## Slide 13: Meteosat-10/SEVIRI FD Winds
WVCT (6.2um)
SWIR (3.9um)
VIS (0.60um)
Low-Level >700 mb
Mid-Level 400-700 mb
High-Level 100-400 mb
LWIR (10.8um)
January 6, 2013)
13
Notes: The Winds Team has been routinely generating experimental winds from GOES-13, GOES-15, Meteosat-9/10/SEVIRI , and NPP/VIIRS using the GOES-R winds algorithm.
Meteosat-10/SEVIRI FD Winds derived rom 0.60um, 3.9um, 6.2um (WVCT & CSWV), 7.3um (CSWV) and 10.8um bands the winds team is routinely generating
13

## Slide 14: Using SEVIRI as a Proxy for the Future GOES-R ABI
Low-Level >700 mb
Mid-Level 400-700 mb
High-Level 100-400 mb
Loop of winds derived from hourly Full Disk Meteosat-9 SEVERI 10.8 µm imagery (22 UTC Apr 24 – 08 UTC Apr 25, 2012
Application of GOES-R Winds Algorithm
to Meteosat/SEVIRI
14

## Slide 15
Cloud-drift winds derived from 15-min GOES-15 imagery over the East Pacific
Low-Level >700 mb
Mid-Level 400-700 mb
High-Level 100-400 mb
Application of GOES-R Winds Algorithm
to Current GOES
15

## Slide 16
Application of GOES-R Winds Algorithm
to Current GOES
Cloud-drift winds derived from 15-min GOES-13 imagery over Hurricane Sandy (4-day loop)
Low-Level >700 mb
Mid-Level 400-700 mb
High-Level 100-400 mb
The GOES-R Winds Team continues to routinely generate and validate ABI proxy winds from GOES-13, GOES-15, Meteosat-10/SEVIRI, and NPP/VIIRS using the GOES-R winds algorithm.
16
Notes: 22 UTC April 24 – 08 UTC April 25, 2012

## Slide 17: NESDIS Operations Plans to Implement an Upgraded GOES Product Processing System Framework
17
Implements Level-2 cloud and derived motion wind algorithm software, developed for the GOES-R ABI, into NESDIS operations for use with the current GOES-N/O/P series
Planned operational date: August 2015
Assures consistency between AMV products generated from GOES-N/O/P series and GOES-R, a likely operational scenario
Will run in parallel with current heritage GOES wind products for 9 months to give NWP users time for testing and switchover activities
Low-Level >700 mb
Mid-Level 400-700 mb
High-Level 100-400 mb
GOES-13 LWIR Winds derived from 10.7µm band over the CONUS sector

## Slide 18
Low-Level >700 mb
Mid-Level 400-700 mb
High-Level 100-400 mb
Application of GOES-R Winds Algorithm to
Simulated GOES-R ABI Imagery
18
Notes: WRF-CHEM Simulated ABI Imagery routinely produced every hour by the GOES-R ABI proxy team.
Initial Capability/Demonstration by AWG proxy team at CIMSS
  WRF-Chem model met/aerosol forecasts (8km) over CONUS using the Community Radiative Transfer Model (CRTM) to simulated all 16 ABI bands.
  NCEP/GFS model 3 hr forecast (T574L64, an effective grid point spacing of ~27 km) outputs used, together with CRTM (v2.1), to produce ABI simulated radiances (all bands) at 3hr intervals over FD
  Generate simulated ABI radiances at 1hr intervals via interpolation of 3hr GFS forecast output and running CRTM every hour
  Simulated data (all bands) are remapped from WRF-chem & GFS grids to the GOES-R ABI fixed grid at their expected resolutions and converted to GRB format

## Slide 19: Winds from VIIRS Derived from the GOES-R Winds Algorithm
19
The VIIRS polar winds product achieved operational status on 8 May 2014.
  VIIRS M15 (10.76um) band used
  First operational use of GOES-R algorithms (clouds, winds)at NESDIS.
  Data distribution via NESDIS’ NDE distribution server & EUMETCAST
September, 2013 – January, 2014

## Slide 20
H-8/AHI Winds
HIMAWARI-8 AHI 1/24/2015 2120 UTC
Low-Level >700 mb
Mid-Level 400-700 mb
High-Level 100-400 mb
20
Band 14 (11um) Winds
Over 50,000 AMVS were generated over the FD (~ 4x increase from current GOES)!!!
These winds were generated using 3 FD images separated by 10 minutes.
Image registration for these three images was quite good.
Notes: The Himawari-8 Advanced Himawari Imager (AHI) is in the relatively early stages of in-orbit checkout
Over 50,000 AMVS were generated over the FD (~ 4x increase from current GOES)
These winds were generated using 3 FD images separated by 10 minutes. Image registration for these three images was quite good.

## Slide 21: Assessing the Quality of Satellite Derived Winds
  Radiosonde Wind Observations
    Used by all operational satellite processing centers that generate satellite derived motion winds
  NCEP GFS Analyses Winds
    Useful over ocean
  Aircraft Communications and Addressing System (ACARS) Wind Observations
21
Notes: Satellite-derived winds and these reference wind observations are collocated in space and time

## Slide 22: Assessing the Quality of Satellite Derived Winds (vs radiosondes)
  100-400 mb
Mean Vector Difference
Speed Bias
Overall Metrics for the Period:
MVD = 4.84 m/s
NRMS = 0.37
Speed Bias = -0.72 m/s
Avg Speed = 16.12 m/s
N = 23,400
22
Meteosat-10/SEVIRI Winds (10.8um)
Notes: Satellite-derived winds and these reference wind observations (radiosondes in this case) are collocated in space and time.
We can do the same comparison for aircraft wind observations…

## Slide 23: User Readiness Activities for GOES-R Winds
23

## Slide 24
User Readiness Activities for
GOES-R Winds
Coordination with GOES-R PG Liaisons to acquire GOES-13/15 winds (generated via GOES-R Winds Algorithm) from STAR and bring them into OPC, AWC, and NHC
Nearing completion of the GOES-R3 Project aimed at readying NCEP for Assimilation of GOES-R AMVs in NCEP’s GFS/GSI
  Project Title: “Development of Advanced Data Assimilation Techniques for Improved Use of Satellite-Derived Atmospheric Motion Vectors”
  Participants: Sharon Nebuda (CIMSS), Jim Jung (CIMSS), Jaime Daniels (NESDIS/STAR), and Wayne Bresky (IMSG)
  Work being done in close collaboration with NCEP personnel
  Successful development and testing of GOES-R AMV quality control procedures that are being adopted at NCEP
  Prepare NCEP for ingest of GOES-R wind products
Application of GOES-R wind algorithm to Himawari-8/AHI
  Completed modifications to winds software for H-8/AHI; successfully generated H-8 winds
  Working to establish routine H-8 winds processing at STAR
  Will provide NWS with H-8 AMV datasets for NWS testing of AWIPS-2 plug-in
24

## Slide 25: Questions
25